## Slide 1: PinK: High-speed In-storage Key-value store with Bounded Tails
Presenter: 신호진
ghwls03s@gmail.com or hj03s@naver.com
2021. 01. 11
Im J. S. and Bae J. W., Chanwoo Chung and Arvind
2020 USENIX Annual Technical Conference, July, 2020

## Slide 2
Introduction
Reference
Motivation
Hypothesis Testing
PinK: In-storage Key-value store
Evaluation
Conclusion

## Slide 3: 1. Introduction
The emergence of several types of SSD
SATA SSD
NVMe SSD
ZNS SSD
Key-value SSD

## Slide 4: 1. Introduction
The emergence of several types of SSD
SATA SSD
NVMe SSD
ZNS SSD
Key-value SSD
Block I/O Interface
Expose a linear array of 4KB logical blocks
Flash translation layer(FTL) in the SSD firmware
FTL maintains a mapping table indexed by logical block address
API = READ(), WRITE() …

## Slide 5: 1. Introduction
The emergence of several types of SSD
SATA SSD
NVMe SSD
ZNS SSD
Key-value SSD
Key-value I/O Interface
Container of key-value objects
Labeled by a unique key and contains an associated value
Key (~255B), value (~2MB)
API = GET(), SET() …

## Slide 6: 1. Introduction
Block I/O interface
Key-value I/O interface

## Slide 7: 2. Reference

## Slide 8: 3. Motivation
Most of KV-SSDs are based on hash
Hash-based KV-SSD maintains a hash table in the controller DRAM. => (4TB SSD – 144GB DRAM)
But, not large enough to accommodate all the hash table entries.
Parts of the hash table must be stored in flash.
Data(KV pair)
(5GB)
DRAM(4GB)
Flash
PUT
Hash Table
(4GB)
NAND Flash
(1GB)

## Slide 9: 3. Motivation
Most of KV-SSDs are based on hash
Hash-based KV-SSD maintains a hash table in the controller DRAM. => (4TB SSD – 144GB DRAM)
But, not large enough to accommodate all the hash table entries.
Parts of the hash table must be stored in flash.
Data(KV pair)
(5GB)
DRAM(4GB)
Flash
PUT
Hash Table
(4GB)
NAND Flash
(1GB)
Data GET request
KV Clients
DRAM(4GB)
Flash
Hash Table
(4GB)
NAND Flash
(1GB)
GET

## Slide 10: 3. Motivation
Most of KV-SSDs are based on hash
Hash-based KV-SSD maintains a hash table in the controller DRAM. => (4TB SSD – 144GB DRAM)
But, not large enough to accommodate all the hash table entries.
Parts of the hash table must be stored in flash.
Data(KV pair)
(5GB)
DRAM(4GB)
Flash
PUT
Hash Table
(4GB)
NAND Flash
(1GB)
Data GET request
KV Clients
DRAM(4GB)
Flash
Hash Table
(4GB)
NAND Flash
(1GB)
No matching Data

## Slide 11: 3. Motivation
Most of KV-SSDs are based on hash
Hash-based KV-SSD maintains a hash table in the controller DRAM. => (4TB SSD – 144GB DRAM)
But, not large enough to accommodate all the hash table entries.
Parts of the hash table must be stored in flash.
Data(KV pair)
(5GB)
DRAM(4GB)
Flash
PUT
Hash Table
(4GB)
NAND Flash
(1GB)
Data GET request
KV Clients
DRAM(4GB)
Flash
Hash Table
(4GB)
NAND Flash
(1GB)
GET
Cause expensive flash access and complex hash table management
Or bucket collision and signature collision

## Slide 12: 3. Motivation
Performance Comparison of KV-SSD & Block-SSD

## Slide 13: 3. Motivation
Performance Comparison of KV-SSD & Block-SSD
Then, isn’t KV-SSD
worse than Block-SSD?

## Slide 14: 3. Motivation
Performance Comparison of KV-SSD & Block-SSD
Then, isn’t KV-SSD
worse than Block-SSD?
Log-Structured
Merger tree

## Slide 15: 3. Motivation
LSM-Tree(Log-Structured Merge Tree)
  Indices KV pairs in a multi-level sorted tree
  Required much smaller DRAM for indexing KV pairs
But Conventional LSM-tree showed worse performance than hash
  Probabilistic nature of Bloom Filter
  High write amplification
  Rebuilding bloom filter and sorting KV pairs for compaction
LSM-Tree abstract

## Slide 16: 3. Motivation
Propose an LSM-tree-based in-storage key-value store engine, called PinK
  Level pinning – instead of keeping probabilistic Bloom filter
  Reduce flash I/Os caused by compaction
  Reduce GC I/Os by delaying index update operations
  Hardware comparators - Accelerator
BTS
COVID-19
Stock
Samsung
Twice
Bitcoin

## Slide 17: 4. Hypothesis Testing
LSM-Tree Unique properties
  For each level KV objects are unique and kept sorted by their key
  The key range of one level may overlap the key range of other levels due to overlap

## Slide 18: 4. Hypothesis Testing
LSM-Tree Unique properties
  For each level KV objects are unique and kept sorted by their key
  The key range of one level may overlap the key range of other levels due to overlap

## Slide 19: 4. Hypothesis Testing
Performance Analysis
  BF = Bloom Filter, YCSB-C = Read 100%
  W = with, W/O = without

## Slide 20: 4. Hypothesis Testing
Observed Problem
  Higher average-latency because of multi-level search, unpredictable tail latency because of Bloom filter
  Bloom filter require lots of computational power to reconstruct
  Level compaction also requires a lot of computation and I/O bandwidth
  Compaction I/Os may trigger GC -> High write amplification

## Slide 21: 5. PinK: In-storage Key-value store
Design of PinK
  Eliminate Bloom filter -> keep popular KV indices in DRAM
  Mitigate the increased read latency by pinning top-K levels
Benefits for level pinning
  Eliminates the flash I/Os required for compaction
  Throughput can be further improved by using hardware accelerators
  Alleviate the GC costs associated with compaction – delay GC

## Slide 22: 5. PinK: In-storage Key-value store
5.1 Overall Architecture
  Skiplist, levellist, meta segment, data segment
Figure 4 : An overall architecture of PinK with its ket data structure in DRAM and flash

## Slide 23: 5. PinK: In-storage Key-value store
5.1 Overall Architecture
  Skiplist
    Corresponds to L0
    L0 size – 8MB ~ 64MB
    Four fields <key size; key; value size; value>
  Levellist
  Meta segment
  Data segment

## Slide 24: 5. PinK: In-storage Key-value store
5.1 Overall Architecture
  Skiplist
    Corresponds to L0
    L0 size – 8MB ~ 64MB
    Four fields <key size; key; value size; value>
  Levellist
    In-memory data structure, keep track of meta segment, except L0
    Each levellist is organized as an array of pairs of fixed-size pointer (4B each, 8B total)
    (physical location of a meta segment, start key of a meta segment)
  Meta segment
  Data segment

## Slide 25: 5. PinK: In-storage Key-value store
5.1 Overall Architecture
  Skiplist
    Corresponds to L0
    L0 size – 8MB ~ 64MB
    Four fields <key size; key; value size; value>
  Levellist
    In-memory data structure, keep track of meta segment, except L0
    Each levellist is organized as an array of pairs of fixed-size pointer (4B each, 8B total)
    (physical location of a meta segment, start key of a meta segment)
  Meta segment
    Contains keys and pointers to its associated values in data segment
    Fixed to flash page size (8KB ~ 16KB)
    <key, pointer> = <16B~128B, 4B integer> + header
  Data segment

## Slide 26: 5. PinK: In-storage Key-value store
5.1 Overall Architecture
  Skiplist
    Corresponds to L0
    L0 size – 8MB ~ 64MB
    Four fields <key size; key; value size; value>
  Levellist
    In-memory data structure, keep track of meta segment, except L0
    Each levellist is organized as an array of pairs of fixed-size pointer (4B each, 8B total)
    (physical location of a meta segment, start key of a meta segment)
  Meta segment
    Contains keys and pointers to its associated values in data segment
    Fixed to flash page size (8KB ~ 16KB)
    <key, pointer> = <16B~128B, 4B integer> + header
  Data segment
  L0 and levellist are protected by capacitor
  Dose not need WAL(write-ahead-log) – provide atomicity and durability of data

## Slide 27: 5. PinK: In-storage Key-value store
5.2 Improving I/O Speed with Level pinning
  Eliminating Read Tails
    Get rid of Bloom filter, adopts level pinning
    Keeps meta segments for top-k levels in DRAM
    Worst case flash lookups is reduce to O(h-k-1)
  Level-pinning Memory Requirement
    The level pinning require large amounts of DRAM? No
    Level size increases exponentially by a factor of T
  Reducing Compaction I/Os
    Eliminates flash I/Os involved in compaction
    Meta segment can be updated in DRAM directly
Before compaction
After compaction

## Slide 28: 5. PinK: In-storage Key-value store
5.2 Improving I/O Speed with Level pinning
  Eliminating Read Tails
    Get rid of Bloom filter, adopts level pinning
    Keeps meta segments for top-k levels in DRAM
    Worst case flash lookups is reduce to O(h-k-1)
  Level-pinning Memory Requirement
    The level pinning require large amounts of DRAM? No
    Level size increases exponentially by a factor of T
  Reducing Compaction I/Os
    Eliminates flash I/Os involved in compaction
    Meta segment can be updated in DRAM directly
Before compaction
After compaction

## Slide 29: 5. PinK: In-storage Key-value store
5.2 Improving I/O Speed with Level pinning
  Eliminating Read Tails
    Get rid of Bloom filter, adopts level pinning
    Keeps meta segments for top-k levels in DRAM
    Worst case flash lookups is reduce to O(h-k-1)
  Level-pinning Memory Requirement
    The level pinning require large amounts of DRAM? No
    Level size increases exponentially by a factor of T
  Reducing Compaction I/Os
    Eliminates flash I/Os involved in compaction
    Meta segment can be updated in DRAM directly
Before compaction
After compaction

## Slide 30: 5. PinK: In-storage Key-value store
5.3 Optimizing Search Path
  Problem
    Level size increase by a factor of T -> O(h^2*log(T))
  Solution
    Using a prefix a key (4B of a start key, while binary search)
    By borrowing fractional cascading technique
    Only L1 maintain range pointer

## Slide 31: 5. PinK: In-storage Key-value store
5.4 Speeding up Compaction

## Slide 32: 5. PinK: In-storage Key-value store
5.4 Speeding up Compaction
ⓐ

## Slide 33: 5. PinK: In-storage Key-value store
5.4 Speeding up Compaction
ⓑ

## Slide 34: 5. PinK: In-storage Key-value store
5.4 Speeding up Compaction
ⓒ

## Slide 35: 5. PinK: In-storage Key-value store
5.4 Speeding up Compaction
ⓓ

## Slide 36: 5. PinK: In-storage Key-value store
5.4 Speeding up Compaction
ⓔ

## Slide 37: 6. Evaluation

## Slide 38: 6. Evaluation

## Slide 39: 6. Evaluation

## Slide 40: 6. Evaluation

## Slide 41: 6. Evaluation

## Slide 42: 6. Evaluation

## Slide 43: 7. Conclusion
Presented a novel LSM-tree-based KV-SSD design, called PinK
By pinning KV indices of top levels of the LSM tree to DRAM, guarantee the worst-case read latency, while improving average read latency
Not only eliminated sorting overheads, but reduced I/O operations related to compaction greatly

## Slide 44: PinK: High-speed In-storage Key-value store with Bounded Tails
Presenter: 신호진
ghwls03s@gmail.com or hj03s@naver.com
2021. 01. 11
Im J. S. and Bae J. W., Chanwoo Chung and Arvind
2020 USENIX Annual Technical Conference, July, 2020
Thank You!